## Slide 1: Laha: A Framework for adaptive optimization of distributed sensor frameworks
Anthony christe
24 February 2020

## Slide 2: Distributed sensor networks
Convert physical phenomena into actionable insights
Dynamic
Heterogenous
Explosion of internet connected sensors
Increased bandwidth, storage, and computational requirements
Incomplete or incorrect data
Lots of primitive data, few insights

## Slide 3: Laha: addressing DSN issues
Laha is an abstract distributed sensor framework that
  Transforms primitive sensor data into actionable insights
  Management of sensor data storage, retention, and analysis
  Scales with minimal system degradation
  Is general enough to apply to multiple DSN domains
  Works with heterogenous and dynamic sensors
  Provides predictive analytics
  Provides self-optimization capabilities

## Slide 4: Laha: A Framework for addressing DSN issues
These capabilities were evaluated and tested in the following ways:
  Design of two Laha-compatible DSNs
  Deployment of two Laha-compatible DSNs
  Validation of data collected by deployments
  Evaluation of major goals of Laha
  Results showing the effectiveness of Laha through the results and evaluation of the Laha-compatible DSNs

## Slide 5: Major claims of the laha framework
General and useful framework for multiple DSN domains
Convert primitive sensor data into actionable insights
Tiered management of Big Data
Tertiary goals and claims. Optimization of:
  Triggering
  Detection/Classification
  Predictive analytics
  Sensing field topology

## Slide 6: Contribution #1: Laha design
Novel abstract distributed sensor framework
  Converting primitive data into actionable insights
  Sensor data management
  Self-optimization capabilities

## Slide 7: Contribution #2: Laha Evaluation
Deployment of two Laha-compatible DSNs
Validated data collection
Several experiments that test Laha’s major claims

## Slide 8: Contribution #3: Laha-compliant reference implementations
OpenPowerQuality (OPQ)
  Distributed power quality (PQ) detection and analysis
Lokahi
  Distributed infrasound detection and analysis

## Slide 9: Contribution #4: Implications for modern DSNs
A set of implications for modern DSNs through the evaluation of Laha
  Confirmation or denial of Laha’s benefits in relation to DSNs
  Other domains that Laha is useful or not useful for

## Slide 10: Related work

## Slide 11: Design: Big data management in Laha
Primitive data into the bottom
Actionable insights out the top
Self-optimization from Phenomena

## Slide 12: Design: Phenomena
Phenomena provide
  Self-optimization
  Actionable insights through
    Predictive analytics
    Ability to group data
Phenomena
  Annotation
  Locality
  Periodic
  Similarity
  Future

## Slide 13: Design of OPQ
OPQ consists of distributed services
  Box
  Makai/Napali
  Mauka
  Health
  View
  MongoDB

## Slide 14: OPQ: Box
Open Source PQ Sensor
12 kHz sampling
Wireless encrypted comms.
Trigger based acquisition
Negrashov 2020

## Slide 15: OPQ: Makai/napali
Data acquisition
Triggering
Box communication broker
Negrashov 2020

## Slide 16: OPQ: mauka
PQ Analysis
Predictive Analytics
Garbage Collection
PQ Plugins (Laha Actors) Providing:
  Annotations, base, box optimization, frequency analysis, future phenomena, IEEE1159 voltage analysis, ITIC classification, GC, Makai Event service, mocking capabilities, outage detection periodicity analysis, debugging, Semi-F47 classification, system health/status, metric collection, THD analysis, threshold optimization, transient detection, and triggering

## Slide 17: OPQ: Health
Box Monitoring
Service Monitoring
Configurable Alerts

## Slide 18: OPQ: view

## Slide 19: Design of lokahi
Lokahi is made up of several distributed services
  Lokahi Sensors
  Time Synch Service
  Acquisition Service
  Web Service
  Analysis Service
  Collaboration Service

## Slide 20: Lokahi: sensors

## Slide 21: Lokahi: time synchronization

## Slide 22: LOKAHI: Web

## Slide 23: Lokahi: Analysis

## Slide 24: Lokahi: collaboration

## Slide 25: Evaluation: Deployment of laha reference implementations
OPQ UHM Locations
  Accessibility
  Co-location with UHM sensors
  Topology of UHM micro-grid
Lokahi Locations
  Ad-hoc public sensor data

## Slide 26: Evaluation of data validation
OPQ
  Compare against GE PQMII & GE EPM7000
Lokahi
  Asmar 2019

## Slide 27: Evaluation of generality of laha framework

## Slide 28: Evaluation of converting primitive data into actionable insights

## Slide 29: Evaluation of big data sensor management

## Slide 30: Evaluation of tertiary goals

## Slide 31: Results of data validation

## Slide 32: Results of generality of laha

## Slide 33: Results of converting primitive data into actionable insights

## Slide 34: Results of tiered management of big data

## Slide 35: Results of tertiary goals

## Slide 36: conclusions

## Slide 37: Future directions
Machine learning
Modifying windows and thresholds
Additional simulations
Altering the Level-hierarchy
Enhanced metric collection
Expanded sensor coverage